Accelerometer & Tacho Sensor

Accelerometer:

- Piezoelectric

- Shear mode

- Wide frequency range

- More than 10 models

- Ground isolated optional

- Low temperature

sensitivity

- Reliable for field use

Specifications:

| Parameter | L14 | L14A | L14B |
| --- | --- | --- | --- |
| Sensitivity, 25oC (pC/ms-2) | 3.5~5.2 | 3.5~5.2 | 3.5~5.2 |
| Freq. Response,+5%（Hz） | 2~5000 | 2~3000 | 2~5000 |
| Freq. Response,+10%（Hz） | 2~10000 | 2~5000 | 2~10000 |
| Vibration limit(m/s2) | 2000 | 2000 | 2000 |
| Transverse sensitivity, max | 5% of axial | 5% of axial | 5% of axial |
| Temperature Range (oC) | –20～＋100 | –20～＋100 | –20～＋100 |
| Case material | Stainless Steel | Stainless Steel | Stainless Steel |
| Weight (g) | 22 | 30 | 22 |

# Text boxes

Model

GND

Power +5Vdc

Output

Tacho Sensor:

- Sensing reflecting light from mark on rotating shaft to supply trigger or rotating speed signal.

- Output signal: TTL

- Indicator: LED, flash when there is an impulse

- RPM range: 60 ~ 24000 r/minute

- Laser distance to the shaft: 30~150 mm

- Power source: 4.5~5.5Vdc, 28mA

- Dimension (mm): 95(Length) × 36(width) × 27(High)

- Weight: 50g